## Slide 1: TrAF-Cloud WP5 – Proof of Concept 1
Current state of the PoC, and
Next steps
2021-03-08
Niklas and Milin

## Slide 2: Outline
Overview TrAF-Cloud Project targets and TrAF-Cloud PoC plans
The first PoC, target and design
PoC 1 demo and rundown
Discussion, PoC 2 targets
Conclusion

## Slide 3: Overview TrAF-Cloud Project targets and TrAF-Cloud PoC plans

## Slide 4: Project Targets Overview From Proposal & kvalitetsgransking@FFI
TrAF-Cloud Goals
Make vehicle and cloud part of the same architecture
To fully utilize combined cloud and truck eco-system, they must follow the same design patterns
Seamless allocation of functionality
Current truck architecture is signal-based and static
Migrate to SoA, adhere to cloud architectural principles
Demonstrator Deliveries
Demonstrate and evaluate the viability of a business-oriented ecosystem for transport cloud services
”
PoC focus
Demonstrate a reference platform that integrates on-board and off-board functionality based on selected use cases
Effect Goals
Faster deployment and integration of new functionality;
The possibility of collecting and sharing large scale of data;
Access to computational resources not available on-board;
Creation of functionality that spans multiple vehicles;
Highly scalable data storage, processing and analytics capabilities.

## Slide 5: PoC—Focus and Iterations
  Demonstrate a reference platform that integrates on-board and off-board functionality based on a selected use cases
  Demonstrator 1 D5.2 (MS3, 21Q2) – Targets
    Establish basic functionality; integrate onboard and offboard communication patterns
    Show that onboard funtionality can be invoked from offboard service
    Show how to leverage SoA principles of Adaptive AUTOSAR
    Show how to leverage MDA-techniques for faster development and deployment
  Next demonstrators
    Demonstrator 2 (D5.3, MS4 21Q4); targets to be disussed after demo
    Innovation challenge (D5.4, MS5 22Q2); may not be feasible, plan for additional demo iteration?
    Final demonstrator (D5.5, MS6 22Q4)

## Slide 6: The first PoC, target and design

## Slide 7: PoC—Premises
Three deployment environments
ECU software
Embedded software, distributed platform, ECUs running (classic and adaptive) AUTOSAR, embedded Linux
Limited memory and compute
Hard real-time, safety critical
Long dev. & depl. cycles
Onboard
Offboard
Cloud environment
“Cloud software”
Very scalable memory and compute resources
Multiple vehicles accessible
Short dev. & depl. cycles
Edge Node
“Cloud Software”
Limited memory and compute
Short dev. & depl. cycles
  Communication patterns
  Request – Response
    Off-board requests invokation of an onboard service, receives a response
    On-board Edge requests invokation of an onboard service, receives a response
    On-board ECU S/W requests invokation of an onboard service, receives a response
    …
  Publish – Subscribe
    Onboard/Edge/offboard service publishes event notifications
    Subscribing Onboard/Edge/offboard service subscribes to notification
PoC 1
Seamless deployment…
…requires architectural support

## Slide 8: Example Req-resp cases
Onboard
Offboard
  E.g, periodically check current vehicle speed, or request headway lights
  Offboard service is implemented in suitable language (e.g. Python, TypeScript, C++, Java, etc)
    Offboard environment provide native APIs to truck functionality
  TrAF-Cloud architecture responsible for
      Generating APIs for range of languages  Structure and format of Platform Boundary objects consistent
      Middleware to invoke function on vehicle
Request
Response
Onboard
Offboard
  E.g. process diagnostics data; if cloud connectivity -> send/stream data and do processing offboard
  Offboard service offered to ECU software in native format (e.g. SOME/IP)
    For onboard funtionality, offboard service appears as just another implementation @service discovery
  TrAF-Cloud architecture responsible for
    Offering available Edge and Offboard services to ECU software
    Managing service registry
    Managing QoS and routing (black- / brown-out)
Request
Response
PoC 1

## Slide 9: PoC 1 demo and rundown

## Slide 10
onboard
offboard
Service/Endpoint exposed
(Heawayill.SetLightDistribution)
Interface (API)
Implementation
Service/Endpoint proxy exposed
(Heawayill.SetLightDistribution)
Interface (API)
<<calls>>
Edge node (component)
Application X
<<calls>>
AWS IoT Core (middleware)
VGCS
API Gateway
(middleware)
ECU software
PoC 1 is:
API gateway (implemented)
Offboard service proxy (code generated)
Utilizing AWS IoT Core for communication

## Slide 11
Onboard platform
Offboard platform
Service/Endpoint exposed
(Heawayill.SetLightDistribution)
Interface (API)
Implementation
Service/Endpoint proxy exposed
(Heawayill.SetLightDistribution)
Interface (API)
Edge node / platform
Application X
AWS IoT Core
VGCS
ECU software
TrAF-Cloud API Gateway
Network
Middleware
VAS / Functional
SOME/IP
Socket Server
Truck Gateway
Socket Client
MQTT Broker
MQTT Client
Cloud Gateway
Adaptive AUTOSAR

## Slide 12: PoC Example call
PoC implementation
Application X
Authentication
Truck service Proxy
Service Registry
MQTT Broker
Cloud Gateway
Truck Gateway
Service Registry
Some/IP

## Slide 13: PoC 1 – Demo
Offboard
ECU Software
TruckGateway
CloudGateway
API Gateway (Edge)
MQTT
UDP Socket
Some/IP

## Slide 14: Code generation
Interface description in Adaptive AUTOSAR
  Specified in an XML-format
  Mainly for deployment and dependency management
  Contains information to generate API (C++)
  Is part of onboard development workflow (a common well-defined asset)
Useful for TrAF-Cloud
  To generate offboard API in various languages (demonstrated)!
  To generate API gateway components (investigated, but not demonstrated)
  To specify offboard services to be consumed onboard (in theory)
<<document>>
arXML

## Slide 15
<<document>>
arXML
onboard
offboard
Service/Endpoint to be exposed
Eg. Heawayill.SetLightMatrix
Interface (API)
Implementation
<<specifies>>
Service/Endpoint to be exposed
Eg. Heawayill.SetLightMatrix
Interface (API)
<<specifies>>
API-gateway
CloudGW
TruckGW
<<specifies>>
<<document>>
Exposed services
<<configures>>
ServiceRepo
<<code>>
Available services
<<code>>
Available services
<<code>>
Available services
ServiceRepo
<<deploy>>
<<calls>>
<<calls>>
<<calls>>
<<generate>>
<<Bold>> -> design-time
<<italics>> -> run-time
App A
App B
<<calls>>
<<calls>>
Code generation PoC 1

## Slide 16: Code generation

## Slide 17: Conclusion

## Slide 18: Summary
“Vehicle and Cloud part of the same architecture” & “Creation of functionality that spans multiple vehicles”
  Middleware to expose vehicle services…
  …native to a range of typical cloud languages/environments
“Faster deployment and integration of new functionality”
  Code generation from common asset  middleware can be auto-generated  Extensibility with minimum of manual effort
  Demonstrates possiblity to integrate in develoment tool-chains
Effect Goals
Faster deployment and integration of new functionality;
The possibility of collecting and sharing large scale of data;
Access to computational resources not available on-board;
Creation of functionality that spans multiple vehicles;
Highly scalable data storage, processing and analytics capabilities.
Make vehicle and cloud part of the same architecture

## Slide 19: Challenges not addressed (yet) Non-exhaustive! Many more can/should be listed!
Middleware
  Authentication and Authorization
    How to manage identities onboard?
    How to manage and enfore access control onboard?
  Service repository management
    How to manage available services (on- and offboard); how to bring up and down services?
Functional architecture
  Request arbitration
    Requests to an onboard service can now come from multiple sources (edge and offboard); how to arbitrate?
  Offboard API design
    The set and structure of onboard service APIs (part of VAS-FuRA?)
  QoS / “Elasticity”(?)
    How to handle blackout, brownout? What middleware support is required?

## Slide 20: Demonstrator 2 (21Q4)
What are the targets for demonstrator 2?
  Proposal 1: “Seamless deployment of services”
    Offboard implementation accessible from onboard
      I.e. transparently offer an offboard implemetation of a known onboard service
    Example: Diagnostics?
    Effect goals: ii, iii, v
  Proposal 2: ?
What has potential to have impact on AB Volvo?
What will raise interest?
Effect Goals
Faster deployment and integration of new functionality;
The possibility of collecting and sharing large scale of data;
Access to computational resources not available on-board;
Creation of functionality that spans multiple vehicles;
Highly scalable data storage, processing and analytics capabilities.

## Slide 21
Onboard platform
Offboard platform
Service/Endpoint exposed
(Heawayill.SetLightDistribution)
Interface (API)
Implementation
Service/Endpoint proxy exposed
(Heawayill.SetLightDistribution)
Interface (API)
Edge node / platform
Application X
AWS IoT Core
VGCS
ECU software
TrAF-Cloud API Gateway
Network
Middleware
VAS / Functional
SOME/IP
Socket Server
Truck Gateway
Socket Client
MQTT Broker
MQTT Client
Cloud Gateway
Adaptive AUTOSAR
Focus can now be on the functional architecture (i.e. VAS-FuRA) with cloud as a deployment environment.
With PoC 2 in place, we have the basic means to quickly test setups…